Perimeter Table ET01P

Technical information
Height	Min 690mm
	Max 940mm
Elevating range	250mm
Elevating speed	Min 15mm/s
Lifting capacity	80kg
Weight	52kg
Height adjustment mechanism	Electrical
Height adjustment control	Switches
Vertical sliding range	140mm
Vertical sliding mechanism	Electrical
Power outlet to instrument	230V 50Hz 500W
Power supply	230V 50Hz

       Optional:

       Foot control set for UP/DOWN movement
       Hand control set for UP/DOWN movement